srvss_pkg containing the following useful parts :

Simulated Environments :

Several simulated environments can be found in the worlds folder. The environments have increasing level of topographical difficulty. The most simple is srvss_world1.world the most topographically difficult is the srvss_world2.world.
You can roslaunch these worlds by :
$ roslaunch srvss_pkg srvss_bobcat_world.launch sw:=[1,2,3,4,5].

Simple autonomous Bobcat :

1. Simple bobcat URDF model with fixed arm and single SICK sensor. In other to use it, just shall run :
  $ rosrun srvss_pkg setupEnv
  Now, if you roslaunch srvss_bobcat_world.launch you will get the simplified bobcat.
2. srvss_rate2efort_node – this node translate the bobcat acceleration and steering commands to bobcat wheels efforts. The difference between this node and the rate2efort node in the bobcat_model package, is that this one considers the physics of bobcat power limitation (Power = Rotation_velocity * Torque). This prevent situations of bobcat throwing itself to air.
  Note : this node do not allow the control of the bobcat arm.

1. srvss_wp_driver_node – this node receive a list of WayPoints and drives the bobcat over them,
  while avoiding obstacles on its path.
  In order to run it type :
  $ rosrun srvss_pkg srvss_wp_driver 10 30 50 60 ....
  (This will cause the bobcat to drive to first WP at lat=10, lon=30 and then to second WP at lat=50, lon=60).
  Note : in order for this to work you should use the srvss_rate2efort node.
2. srvss_wp_keyboard_commander_node - this node reads continuously from the command line new WP coordinates and send them to srvss_wp_driver node.
  $ rosrun srvss_pkg srvss_wp_keyboard_commander_node
  wp_X = 10
  wp_Y = 30

Note : in order for this to work you should rosrun first the srvss_wp_driver_node.